fo

# Text boxes

Dimensions in Inches,   Tolerances:  .XX ( .03    .XXX (  .010

TERMINAL IDENTIFICATION

1.  A.C. INPUT HI

2.  A.C. INPUT LO

3.  CASE GROUND

4.  OUTPUT RETURN

5.  OUTPUT POSITIVE

AC VOLTAGE SENSOR

MODEL 105

PRESET RANGE (VMAX TO VMIN)		MODEL

390 to 490 VRMS			 -490

455 to 505 VRMS			 -505

430 to 530 VRMS                                                    -530

400 to 560 VRMS			 -560

INPUT LINE FREQUENCY		57 to 63Hz

EXCITATION		Self-excited

BURDEN		1Va Typical

OUTPUT FOR PRESET RANGE		0 to 5Vdc

OUTPUT IMPEDANCE		3K Ohms Max.

RESPONSE		Within 1 Cycle of Input Frequency

RIPPLE		50mV RMS

SUPPRESSION VOLTAGE ACCURACY		± .25% of V Min.

RANGE ACCURACY		± 0.5% F.S. Max.

TEMPERATURE COEFFICIENT		± .08% F.S. per °C

TEMPERATURE RANGE		-40 to +85°C

WEIGHT		20oz. Max.

* OTHER PRESET RANGES AVAILABLE

AAC

Drawing Number	Rev.

700-105	L